OPHAF version 0.20
Open Protocol for Home Automation and Flexibility

This protocol is used to communicate between a home automation system and appliances, sensors and information servers.

JSON	JSON is used for the communication

Standard keys	Every message should contain the messagenumber, key: “message” / A response had a messagenumber 50 higher / If the key “id” is used in the initial message, the reply should contain the same response / The key “remark” can be used for human readability, but has no meaning / The reply can have key “error” when not executed, with values 1: command not found, 2: values not understood. 3: “value not possible to execute”. Optional the key “errortext” gives a description. / The reply can have key “warningtext”; the command is however executed (unless error was given”. / The messages can have key “debugtext” for debug information; as “remark” is has no meaning.
Multiple devices	An appliance can contain multiple devices. The “device” key can be used. Omitting “device” addresses the default device (or only device)

Units	All numbers with physical meaning should have units / There can be a space between number and unit, but is not needed / Values are given as string
Energy	J, KJ, MJ
Power	W, KW, MW
Temperature	C, F
Time	s, m, h, d. Can be combined, no decimal point allowed (except s) / Relative times to now, are given with 0+ (future) or 0- (past) (eg. “0-15m” means 15 minutes ago) / A duration can also contain “infinity”.
Date	Date is given in ISO 8601 notation: 24h format as “YYYY-MM-DD HH:MM:SS” / Depending on use vales from left and right side may be omitted:, eg: / DD HH:MM:SS / YYYY-MM-DD HH / MM-DD HH:MM
Percentage	%
State	“on” or “off”
Logical	“true” or “false”

Commands

0 / 50	Ping and get version / Reply is number. This version is 0.20 / Example: / { “message”: 0, “id”: “abcd”, “remark”: “ping” } / { “message”: 50, “id”: “abcd”, “version”: 0.20 }
1 / 51	Get info / Reply is type number / -1: list / 0: Generic / 1: EV / 2: Solar / 3: Heating / cooling / 4: Washing / Machine is free text / If one interface contains more devices, a list is given with the letters. / Examples / { “message”: 1 } / { “message”: 51, “type”: 1, “machine”: “ACME RB2000”} / Reply from an integrated solar / cooling unit: / { “message”: 51, “machine”: “ACME RB2000 Plus” / “typelist”: [ {“type”: 2, “device”: 1}, {“type”: 3, “device”: 2} ] }
2 / 52	Get command list / Reply is list with supported optional commands for the specified type / Example: / { “message”: 2, “device”: 1 } / { “message”: 52, “device”: 1, “commandlist”: [“command”: 105, “command”: 106]}
3 / 53	Get status / Reply is number: / 0: not ready (off, no user selection, etc) / 1: ready (to start) / 2: active / Example / { “message”: 3, } / { “message”: 53, “status”: 2 }

10 / 60	Switch / keys: “switch” with options ”on”, “off” or percentage / Example / { “message”: 10, “switch”: “25%” } / { “message”: 60 }
11 / 61	Get switch / Replies switch status / Example / { “message”: 11} / { “message”: 61, “switch”: “25%” }
12 / 62	Get sensor / Gives the sensor data. Main keys are “sensor” and “sensorlist”. A sensor dataset contains “value” and optional “id”. / Examples / { “message”: 12} / { “message”: 62, “sensor”: {“value”: “21.3C”} } / { “message”: 12} / { “message”: 62, / “sensorlist”: [{“value”: “20.6C”, “id”: “Internal”}, / {“value”: “12.1C”, “id”: “External”}, / {“value”: “12.9C”, “id”: “Air inlet”}] / }
13 / 63	Get sensor history / Gives the historic sensor data. Main keys are “sensordata” and “sensordatalist”. The list contains “value” and optional “description”, “time”, “date”. / Example / { “message”: 13} / { “message”: 63, / “sensordata”: [{“value”: “20.9C”, “time”: “0-15m”}, / {“value”: “20.5C”, “time”: “0-30m”}, / {“value”: “20.2C”, “time”: “0-45m”}, / {“value”: “20.0C”, “time”: “0-60m”}] / } / { “message”: 13} / { “message”: 63, / “sensordatalist”: [ “id”: “Internal”, / [ {“value”: “20.9C”, “time”: “0-15m”}, / {“value”: “20.5C”, “time”: “0-30m”}, / {“value”: “20.2C”, “time”: “0-45m”}, / {“value”: “20.0C”, “time”: “0-60m”}] ], / “id”: “External”, / [ {“value”: “12.2C”, “time”: “0-15m”}, / {“value”: “12.3C”, “time”: “0-30m”}, / {“value”: “12.3C”, “time”: “0-45m”}, / {“value”: “12.4C”, “time”: “0-60m”}] ] / }
20 / 70	Get forecast servicelist / This can be used at servers to obtain forecast services / Example / { “message”: 20} / { “message”: 70, / “servicelist”: [{“service”: “temperature”, / “service”: “electricityprices”, / “service”: “wind” ] / }
21 / 71	Get forecast service / This can be used at servers to obtain forecast services / Example / { “message”: 21, “service”: “electricityprices”} / { “message”: 71, “service”: “electricityprices”, / “forecast”: [{“date”: “2025-02-03 0:00”, “value”: “0.34 euro/kWh”}, / {“date”: “2025-02-03 1:00”, “value”: “0.22 euro/kWh”}, / {“date”: “2025-02-03 2:00”, “value”: “0.25 euro/kWh”}, / {“date”: “2025-02-03 3:00”, “value”: “0.26 euro/kWh”} ] / }

100 / 150	Get charging mode / key: “mode”. / 0: off (not possible to switch on). / 1: ready to switch on. / 2: switched on. / 3: finished (not possible to switch on). / Example / { “message”: 100} / { “message”: 150, “mode”: 2 }
101/ 151	Switch charging / keys: “switch” with options ”on” and “off” / Example / { “message”: 101, “switch”: “on” } / { “message”: 151 } / { “message”: 101, “switch”: “on” } / { “message”: 151, “error”: 3, “errortext”: “Automatic mode not selected by user”}
102 / 152	Get specs / The specs consist of the following keywords: / Required: / “charging_max” / “discharging_max” / “batterycapacity_max” / Optional: / “charging_peak” / “charging_peaktime” / “discharging_peak” / “discharging_peaktime” / “batterycapacity_min” / Example / { “message”: 102} / { “message”: 152, / “charging_max”: “7.2 kW”, / “discharging_max”: “5.3 kW”, / “batterycapacity_max”: “30 kJ” / }
103 / 153	Get battery status / Reply is capacity in battery with key “charge” / This can be measured or calculated. / Example / { “message”: 103} / { “message”: 153, “charge”: “4.6 kJ” } / Example of two independent batteries: / { “message”: 103} / { “message”: 153, “device“: 1, charge”: “4.6 kJ” } / { “message”: 103, “device“: 2} / { “message”: 153, “device“: 2, charge”: “6.1 kJ” }
104 / 154	Set charging / Set charging level with key “power”. / Positive is charging, negative is discharing / Examples / { “message”: 104, “power”: “4.6 kW”} / { “message”: 154 }
105	Get charging / Reply the power in charging. / The value can be measured or calculated / Example / { “message”: 105 } / { “message”: 155, “power”: “-4.6 kW”}

	Solar, type 2
200 / 250	Get converter mode / key: “mode”. / 0: off (not possible to control). / 1: on (not possible to control). / 2: ready to control. / 3: being controlled. / Example / { “message”: 200} / { “message”: 250, “mode”: 2 }
201/ 251	Switch converter / keys: “switch” with options ”on” and “off” / Example / { “message”: 201, “switch”: “on” } / { “message”: 251 } / { “message”: 201, “switch”: “on” } / { “message”: 251, “error”: 3, “errortext”: “Automatic mode not selected by user”}
202 / 252	Get specs / The specs consist of the following keywords: / Required: / “power_max” / Optional: / “power_peak” / “power_peaktime” / Example / { “message”: 202} / { “message”: 252, “power_max”: “3.2 kW” }
203 / 253	Get actual / Example / { “message”: 203} / { “message”: 253, “power_panel”: “1.3 kW”, / “power_converter”: “1.3 kW”, / “power_max”: “3.2 kW” }
204 / 254	Get converter output / Example / { “message”: 204} / { “message”: 204, “power_converter”: “2.3 kW” }
205 / 255	Set maximum converter output / { “message”: 205, “power_max”: “2.9 kW”} / { “message”: 255 }

	Heating / cooling, type 3
300 / 350	Get mode / key: “mode”. / 0: off (not possible to control). / 1: on (not possible to control). / 2: ready to control. / 3: being controlled. / Example / { “message”: 300} / { “message”: 350, “mode”: 3 }
301/ 351	Switch / keys: “switch” with options ”on” and “off” / Example / { “message”: 301, “switch”: “on” } / { “message”: 351 }
302 / 352	Get specs / The specs consist of the following keywords: / Keys: / “heating_power_max” / “cooling_power_max” / Example / { “message”: 302} / { “message”: 352, / “heating_power_max”: “1.8 kW”, / “cooling_power_max”: “1.2 kW” / }
303 / 353	Get actual / Example / { “message”: 203} / { “message”: 253, “heating_power”: “1.3 kW”, / “cooling_power”: “0.0 kW”, / “heating_power_max”: “1.8 kW”, / “cooling_power_max”: “1.2 kW” / “manual_setpoint”: “21.0 C” / “temperature”: “19.5 C” }
304 / 354	Set heating / Set heating with key “heating_power”. / Switch off cooling / Examples / { “message”: 304, “heating_power”: “0.4 kW”} / { “message”: 354 }
305 / 355	Set cooling / Set cooling with key “cooling_power”. / Switch off heating / Examples / { “message”: 305, “cooling_power”: “1.0 kW”} / { “message”: 355 }

	Dishwasher, washing machine, dryer, type 4
400 / 450	Get charging mode / key: “mode”. / 0: off (not possible to control). / 1: ready to switch on. / 2: switched on (being controlled). / 3: finished (not possible to switch on). / Example / { “message”: 400} / { “message”: 450, “mode”: 1 }
401/ 451	Switch charging / keys: “switch” with options ”on” and “off” / Example / { “message”: 401, “switch”: “on” } / { “message”: 451 }
402 / 452	Get program profile / for “selected” see 404 / Example / { “message”: 402 } / { “message”: 452, / “program”: [{“step”: 1, “duration”: “25 m”, “power”: “1.2 kW” }, / {“step”: 2, “pause”: “15 m”, “max_pause”: “30 m”, }, / {“step”: 3, “duration”: “35 m”, “power”: “0.4 kW” }, / {“step”: 4, “pause”: “0 s”, “max_pause”: “infinity” }, / {“step”: 5, “duration”: “20 m”, “power”: “0.1 kW” } ] / }
403 / 453	Get program progress / Example / { “message”: 403 } / { “message”: 453, “step”: 3, “remaining”: “12 m 34 s” }
404 / 454	Control program / Set pause time in program. Message 452 shows whether pause is set / Example / { “message”: 404, “pause_at_step”: 2, “duration”: “15 m” } / { “message”: 454 }